## Slide 1: Exception
Yubin Xia
IPADS, SJTU
ACKs: Some slides are adapted from the textbook’s original slides and Frans’s os course notes

## Slide 2: Review: IPC
Cooperating processes need inter-process communication (IPC)
Two models of IPC
  Shared memory
  Message passing
In POSIX
  Pipe, msg passing, signal, shared memory, semaphore, etc.
LRPC: Lightweight RPC

## Slide 3: Concepts
Exception
  refers to an illegal program action
Interrupt
  refers to a signal generated by a hardware device
System call
  a user program can ask for an operating system service

## Slide 4: Exception

## Slide 5: CPU’s ‘fetch-execute’ cycle
Fetch instruction at IP
Advance IP to next instruction
Decode the fetched instruction
Execute the decoded instruction
Interrupt?
no
Save context
Get INTR ID
Lookup ISR
Execute ISR
yes
IRET
User
Program
IP
ld
add
st
mul
ld
sub
bne
add
jmp
…

## Slide 6: Exception Table
1. Each type of event has a unique exception number k
2. Exception table entry k points to a function (exception handler).
3. Handler k is called each time exception k occurs.
Exception
table
0
1
2
...
n-1
code for
exception handler 0
code for
exception handler 1
code for
exception handler 2
code for
exception handler n-1
...
Exception
numbers

## Slide 7: Exception Table

## Slide 8: Some Exception on Intel CPU
Notes: Questions:
What is the difference between an exception and an interrupt caused by hardware?
Can system call be implemented by using int 0x81 or 0x82?

## Slide 9: IDT (or Trap Vector in xv6)
IDT: interrupt descriptor table
  Another name of exception table
  Has 256 entries
  Each giving the %cs and %eip to be used when handling the corresponding interrupt
System call
  A program invokes int n
  n specifies the index into the IDT

## Slide 10: Exception Handler
The processor pushes a return address on the stack, the return address is
  either the current instruction
  or the next instruction
The processor also pushes some additional processor state onto the stack
  will be necessary to restart the interrupted program when the handler returns
    e.g. the current condition codes

## Slide 11: Exception Handler
All items are pushed onto the kernel stack
  Rather than onto the user’s stack
    If control is being transferred from a user program to the kernel
Exception handlers run in kernel mode
  Means they have complete access to all system resources

## Slide 12: Kernel Stack

## Slide 13: Stack Change
Question: why not use user’s stack?
执行完之后有IRET指令，这个指令室内和权限执行的 ，所以如果在
用户栈上，用户可能会做ROP攻击。

## Slide 14: Sources of Events cause User->Kernel
Device interrupt: external
  Nonmaskable interrupt (NMI) input pin
  Interrupt (INTR) input pin
Software interrupt: execution of the Interrupt instruction
  e.g., INT
Program faults: If some error condition occur by the execution of an instruction. E.g.,
  divide-by-zero interrupt

## Slide 15: What Has to Happen?
Must save the processor’s registers for future transparent resume
Must be set up for execution in the kernel
Must chose a place for the kernel to start executing
Must be able to retrieve information about the event, e.g., system call arguments
Must all be done securely
Must maintain isolation of user processes and the kernel

## Slide 16: Return From Interrupt Handler in Kernel
The ‘iret’ instruction
  Restore the process’s context
  Switch from kernel mode to user mode
  Continue the execution of user’s process

## Slide 17: Simplified: Call OS Services from Apps and Devices
Exception
Table
Application (CPU)
OS
I/O Device
Services
Exception
Interrupt
Notes: Question: what if

## Slide 18: xv6: Initialize the Exception Table

## Slide 19: xv6: Trap

## Slide 20: Interrupt

## Slide 21: Varying Terminology for Intel
Interrupts (asynchronous, device generated)
  Maskable: device-generated, associated with IRQs (interrupt request lines); may be temporarily disabled (still pending)
  Nonmaskable: some critical hardware failures
Exceptions (synchronous, from software)
  Processor-detected
    Faults – correctable (restartable); e.g. page fault
    Traps – no reexecution needed; e.g. breakpoint
    Aborts – severe error; process usually terminated (by signal)
  Programmed exceptions (software interrupts)
    int (system call), int3 (breakpoint)
    into (overflow), bounds (address check)

## Slide 22: Terms
Vector, Interrupt vector, Trap number
IRQ: Interrupt Request
(Soft IRQ: A mechanism to implement bottom half)
  Has nothing to do with IRQ!
Interrupt, trap, fault, exception
Software interrupt / system call
IDT: Interrupt Descriptor Table
ISP: Interrupt Service Procedure

## Slide 23: Intel-Reserved ID-Numbers
Of the 256 possible interrupt ID numbers, Intel reserves the first 32 for ‘exceptions’
OS’s such as Linux are free to use the remaining 224 available interrupt ID numbers for their own purposes (e.g., for service-requests from external devices, or for other purposes such as system-calls)
Examples:
  0: divide-overflow fault
  6: Undefined Opcode
  7: Coprocessor Not Available
  11: Segment-Not-Present fault
  12: Stack fault
  13: General Protection Exception
  14: Page-Fault Exception

## Slide 24: Interrupts
Interrupts are similar to system calls, except devices generate them at any time
There is hardware on the motherboard to signal the CPU when a device needs attention (e.g., the user has typed a character on the keyboard)
We must program the device to generate an interrupt, and arrange that a CPU receives the interrupt

## Slide 25: Interrupt Response Sequence

## Slide 26: Early Boards
PIC (Programmable Interrupt Controller)
  picirq.c
  8259A chip
  Each PIC handles 8 interrupts, and multiplex them on the interrupt pin of the processor
  PIC can be cascaded
    Master: 0 to 7
    Slave: 8 to 15
  Read timer.c for timer init

## Slide 27: 8259A Programmable Interrupt Controller (PIC)
8259A is a 28-pin integrated circuit which was designed specifically for the 8088/8086 microprocessors
Notes: ❚ The 28 pins of the 8259A include:
1. Data pins D0-D7 - connected to the data bus to allow programming
2. IR0-IR7 - 8 interrupt inputs
3. CAS0-CAS2 - cascade lines (used in multiple 8259A systems)
4. SP/EN - functions as data buffer enable output (when buffered mode)
or as an input to program the 8259A as a master or slave
5. A0 - input which selects different command words in the 8259A
❚ Usually IR0 has the highest priority and IR7 the least priority.
❚ Fully nested interrupts are supported (higher priority interrupts may
interrupt the interrupt service routine of a lower priority interrupt) if bit 4 of
ICW is set. (Refer to data sheets for further details.)

## Slide 28
Interrupt Hardware
x86
CPU
Master
PIC
(8259)
Slave
PIC
(8259)
INTR
Programmable Interval-Timer
Keyboard Controller
Real-Time Clock
Legacy PC Design
(for single-proc
systems)
SCSI Disk
Ethernet
I/O devices have (unique or shared) Interrupt Request Lines (IRQs)
IRQs are mapped by special hardware to interrupt vectors, and passed to the CPU
This hardware is called a Programmable Interrupt Controller (PIC)
IRQs

## Slide 29: APIC, IO-APIC, LAPIC
Advanced PIC (APIC) for SMP systems
  Used in all modern systems
  Interrupts “routed” to CPU over system bus
  IPI: inter-processor interrupt
Local APIC (LAPIC) versus “frontend” IO-APIC
  Devices connect to front-end IO-APIC
  IO-APIC communicates (over bus) with Local APIC
Interrupt routing
  Allows broadcast or selective routing of interrupts
  Ability to distribute interrupt handling load
  Routes to lowest priority process
    Special register: Task Priority Register (TPR), i.e., locking
  Arbitrates (round-robin) if equal priority

## Slide 30: Multiple Processors
Multi-CORE CPU
CPU
0
CPU
1
I/O
APIC
LOCAL
APIC
LOCAL
APIC
Advanced Programmable Interrupt Controller is needed to
perform ‘routing’ of I/O requests from peripherals to CPUs
(The legacy PICs are masked when the APICs are enabled)
Notes: External hardware INTerrupt sources are routed to pins of the IO APIC. These include motherboard sources such as the 8254 timer, as well asISA/PCI card slots. INTerrupts are "collected" by this part, and forwarded via the APIC bus to one or more CPUs when they occur.

## Slide 31: Multi-processor PC Boards
Two parts in XV6
  IO APIC, for the I/O system
    ioapic.c
  Local APIC, for each processor
    lapic.c
XV6 is designed for multi-processor
  Each processor must be programmed to receive interrupts

## Slide 32: Assigning IRQs to Devices
IRQ assignment is hardware-dependent
  Sometimes it’s hardwired, sometimes it’s set physically, sometimes it’s programmable
  PCI bus usually assigns IRQs at boot
Some IRQs are fixed by the architecture
  IRQ0: Interval timer
  IRQ2: Cascade pin for 8259A
Linux device drivers request IRQs when the device is opened
  Note: especially useful for dynamically-loaded drivers, such as for USB or PCMCIA devices
  Two devices that aren’t used at the same time can share an IRQ, even if the hardware doesn’t support simultaneous sharing

## Slide 33: Some Details on IRQ
Some hardware IRQs are pre-determined
  such as the system timer (IRQ0), Keyboard controller (IRQ1),
  floppy controller (IRQ6), real-time clock (IRQ8) and
  Math Co-processor (IRQ13).
Most others are ‘user’ determined
  via hardware (with jumpers)
  via software (such as installable drivers) with firmware (PNP)
IRQs that are usually available for add-on devices:
  Modem (IRQ5), printer (IRQ7), Sound Card (IRQ9/IRQ10),
  Video Card (IRQ11) and PS/2 mouse (IRQ12).
  IRQ3 and IRQ4 are usually reserved for serial ports
  IRQ14 and IRQ15 are used for the IDE (primary and secondary).

## Slide 34: Assigning Vectors to IRQs
Vector: index (0-255) into interrupt descriptor table
Vectors are usually IRQ# + 32
  Below 32 reserved for non-maskable intr & exceptions
  Maskable interrupts can be assigned as needed
  Vector 128 used for syscall
  Vectors 251-255 used for IPI

## Slide 35: Putting It All Together
PIC
CPU
Memory Bus
INTR
0
N
IRQs
IDT
0
255
handler
idtr
Mask points
vector

## Slide 38: Timer Interrupt

## Slide 39: Sleep & Wakeup

## Slide 40: Interrupt Priority
When different types of interrupt (ie. software, NMI, INTR or exceptions) occur at the same time, the one with the highest priority is handled first. Intel microprocessors use the following order of priority:

## Slide 41: EOI: End of Interrupt
Issued to the PIC chips at the end of an IRQ-based interrupt routine
  If the IRQ came from the Master PIC, it is sufficient to issue this command only to the Master PIC;
  If the IRQ came from the Slave PIC, it is necessary to issue the command to both PIC chips

## Slide 42: Nested Interrupts
What if a second interrupt occurs while an interrupt routine is excuting?
Generally a good thing to permit that — is it possible?
And why is it a good thing?

## Slide 43: Maximizing Parallelism
You want to keep all I/O devices as busy as possible
In general, an I/O interrupt represents the end of an operation; another request should be issued as soon as possible
Most devices don’t interfere with each others’ data structures; there’s no reason to block out other devices

## Slide 44: Handling Nested Interrupts
As soon as possible, unmask the global interrupt
As soon as reasonable, re-enable interrupts from that IRQ
But that is not always a great idea, since it could cause re-entry to the same handler
IRQ-specific mask is not enabled during interrupt-handling

## Slide 45: Nested Execution
Interrupts can be interrupted
  By different interrupts; handlers need not be reentrant
  Small portions execute with interrupts disabled
  Interrupts remain pending until acked by CPU
Exceptions can be interrupted
  By interrupts (devices needing service)
Exceptions can nest two levels deep
  Exceptions indicate coding error
  Exception code (kernel code) shouldn’t have bugs
  Page fault is possible (trying to touch user data)

## Slide 46: Interrupt Masking
Two different types: global and selective (per-IRQ)
  Global — delays all interrupts
  Selective — individual IRQs can be masked selectively
  Selective masking is usually what’s needed — interference most common from two interrupts of the same type
NMI (Non-Maskable Interrupt)

## Slide 47: Triple Fault
Things never to do in an OS #1: Swap out the page swapping code (triple-fault here we come) —Kemp
When a fault occurs, the CPU invokes an exception handler.
If a fault occurs while trying to invoke the exception handler, that's called a double fault, which the CPU tries to handle with yet another exception handler.
If that invocation results in a fault too, the system reboots with a triple fault.
Notes: A triple fault is usually a sign that the exception handler called is faulty, or worse, that the whole exception handling in your system is screwed up. (LDT or GDT issues, bogus pointers or faulty memory mappings are frequent offenders.)
Another frequent cause of triple faults is a kernel stack overflow. If the stack reaches an invalid page (one with its present bit clear), a page fault is generated. However, the CPU faults while trying to push the exception information on to the stack, so a double fault is generated. The same problem still exists so a triple fault is generated.

## Slide 48: /proc/interrupts
$ cat /proc/interrupts
CPU0
0: 865119901 IO-APIC-edge timer
1: 4 IO-APIC-edge keyboard
2: 0 XT-PIC cascade
8: 1 IO-APIC-edge rtc
12: 20 IO-APIC-edge PS/2 Mouse
14: 6532494 IO-APIC-edge ide0
15: 34 IO-APIC-edge ide1
16: 0 IO-APIC-level usb-uhci
19: 0 IO-APIC-level usb-uhci
23: 0 IO-APIC-level ehci-hcd
32: 40 IO-APIC-level ioc0
33: 40 IO-APIC-level ioc1
48: 273306628 IO-APIC-level eth0
NMI: 0
ERR: 0
Columns: IRQ, count, interrupt controller, devices

## Slide 49: More in /proc/pci:
$ cat /proc/pci
PCI devices found:
Bus 0, device 0, function 0:
Host bridge: PCI device 8086:2550 (Intel Corp.) (rev 3).
Prefetchable 32 bit memory at 0xe8000000 [0xebffffff].
Bus 0, device 29, function 1:
USB Controller: Intel Corp. 82801DB USB (Hub #2) (rev 2).
IRQ 19.
I/O at 0xd400 [0xd41f].
Bus 0, device 31, function 1:
IDE interface: Intel Corp. 82801DB ICH4 IDE (rev 2).
IRQ 16.
I/O at 0xf000 [0xf00f].
Non-prefetchable 32 bit memory at 0x80000000 [0x800003ff].
Bus 3, device 1, function 0:
Ethernet controller: Broadcom NetXtreme BCM5703X Gigabit Eth (rev 2).
IRQ 48.
Master Capable. Latency=64. Min Gnt=64.
Non-prefetchable 64 bit memory at 0xf7000000 [0xf700ffff].

## Slide 50: Three crucial data-structures
The Global Descriptor Table (GDT)
    defines the system’s memory-segments and their access-privileges, which the CPU has the duty to enforce
The Interrupt Descriptor Table (IDT)
    defines entry-points for the various code-routines that will handle all ‘interrupts’ and ‘exceptions’
The Task-State Segment (TSS)
    holds the values for registers SS and ESP that will get loaded by the CPU upon entering kernel-mode

## Slide 51: How does CPU find GDT/IDT?
Two dedicated registers: GDTR and IDTR
Both have identical 48-bit formats:
Segment Base Address
Segment Limit
0
15
16
47
Privileged instructions: LGDT and LIDT used to set these register-values
Unprivileged instructions: SGDT and SIDT used for reading register-values
Kernel must setup these registers during system startup (set-and-forget)

## Slide 52: How does CPU find the TSS?
Dedicated system segment-register TR holds a descriptor’s offset into the GDT
TR
GDTR
GDT
TSS
The CPU knows the layout
of fields in the Task-State
Segment
The kernel must set up the
GDT and TSS structures
and must load the GDTR
and the TR registers

## Slide 53: Bottom half

## Slide 54: Interrupt Handling Philosophy
Do as little as possible in the interrupt handler
Defer non-critical actions till later
Structure: top and bottom halves
  Top-half: do minimum work and return (ISR)
  Bottom-half: deferred processing (softirqs, tasklets, workqueues, kernel threads)
Top half
softirq
tasklet
workqueue
kernel thread
Bottom half

## Slide 55: Top Half: Do it Now!
Technically is the interrupt handler
Perform minimal, common functions: save registers, unmask other interrupts. Eventually, undoes that: restores registers, returns to previous context.
  Often written in assembler
IRQ is typically masked for duration of top half
Most important: call proper interrupt handler provided in device drivers (C program)
Don’t want to do too much here
  IRQs are masked for part of the time
  Don’t want stack to get too big
Typically queue the request and set a flag for deferred processing in a bottom half

## Slide 56: Top Half: Find the Handler
On modern hardware, multiple I/O devices can share a single IRQ and hence interrupt vector
First differentiator is the interrupt vector
Multiple interrupt service routines (ISR) can be associated with a vector
Each device’s ISR for that IRQ is called
Device determines whether IRQ is for it

## Slide 57
Mechanisms to defer work to later:
  softirqs
  tasklets (built on top of softirqs)
  work queues
  kernel threads
All can be interrupted
Bottom Half: Do it Later!
Top half
softirq
tasklet
workqueue
kernel thread
Bottom half

## Slide 58: Warning: No Process Context
Interrupts (as opposed to exceptions) are not associated with particular instructions
They’re also not associated with a given process (user program)
The currently-running process, at the time of the interrupt, as no relationship whatsoever to that interrupt
Interrupt handlers cannot sleep!

## Slide 59: What Can’t You Do?
You cannot sleep
  or call something that might sleep
You cannot refer to current
You cannot allocate memory with GPF_KERNEL (which can sleep), you must use GPF_ATOMIC (which can fail)
You cannot call schedule()
You cannot do a down() semaphore call
  However, you can do an up()
You cannot transfer data to/from user space
  E.g., copy_to_user(), copy_from_user()

## Slide 60: Interrupt Stack
When an interrupt occurs, what stack is used?
  Exceptions: The kernel stack of the current process, whatever it is, is used (There’s always some process running — the “idle” process, if nothing else)
  Interrupts: hard IRQ stack (1 per processor)
  SoftIRQs: soft IRQ stack (1 per processor)
These stacks are configured in the IDT and TSS at boot time by the kernel

## Slide 61: Softirqs
Statically allocated: specified at kernel compile time
Limited number:
Priority Type
0 High-priority tasklets
1 Timer interrupts
2 Network transmission
3 Network reception
4 Block devices
5 Regular tasklets

## Slide 62: When Do Softirqs Run?
Run at various points by the kernel:
  After system calls
  After exceptions
  After interrupts (top halves/IRQs, including the timer intr)
  When the scheduler runs ksoftirqd
Softirq routines can be executed simultaneously on multiple CPUs:
  Code must be re-entrant
  Code must do its own locking as needed
Hardware interrupts always enabled when softirqs are running

## Slide 63: Rescheduling Softirqs
A softirq routine can reschedule itself
This could starve user-level processes
Softirq scheduler only runs a limited number of requests at a time
The rest are executed by a kernel thread, ksoftirqd, which competes with user processes for CPU time

## Slide 64: Tasklets
Built on top of softirqs
Can be created and destroyed dynamically
Run on the CPU that scheduled it (cache affinity)
Individual tasklets are locked during execution; no problem about re-entrancy, and no need for locking by the code
Tasklets can run in parallel on multiple CPUs
  Same tasklet can only run on one CPU
Were once the preferred mechanism for most deferred activity, now changing

## Slide 65: The Trouble with Tasklets
Hard to get right
One has to be careful about sleeping
They run at higher priority than other tasks in the systems
Can produce uncontrolled latency if coded badly
Ongoing discussion about eliminating tasklets
Will likely slowly fade over time

## Slide 66: Work Queues
Always run by kernel threads
  Are scheduled by the scheduler
Softirqs and tasklets run in an interrupt context; work queues have a pseudo-process context
  i.e., have a kernel context but no user context
Because they have a pseudo-process context, they can sleep
  Work queues are shared by multiple devices
  Thus, sleeping will delay other work on the queue
However, they are kernel-only; there is no user mode associated with it
  Don’t try copying data into/out of user space

## Slide 67: Kernel Threads
Always operate in kernel mode
  Again, no user context
2.6.30 introduced the notion of threaded interrupt handlers
  Imported from the realtime tree
  request_threaded_irq()
  Now each bottom half has its own context, unlike work queues
  Idea is to eventually replace tasklets and work queues

## Slide 68: Comparing Approaches
 | ISR | SoftIRQ | Tasklet | WorkQueue | KThread
Will disable all interrupts? | Briefly | No | No | No | No
Will disable other instances of self? | Yes | Yes | No | No | No
Higher priority than regular scheduled tasks? | Yes | Yes* | Yes* | No | No
Will be run on same processor as ISR? | N/A | Yes | Yes | Yes | Maybe
More than one run can on same CPU? | No | No | No | Yes | Yes
Same one can run on multiple CPUs? | Yes | Yes | No | Yes | Yes
Full context switch? | No | No | No | Yes | Yes
Can sleep? (Has own kernel stack) | No | No | No | Yes | Yes
Can access user space? | No | No | No | No | No
*Within limits, can be run by ksoftirqd