## Slide 1: XV6 & VM
Rong Chen & Yubin Xia
Some slides are based on Frans Kaashoek’s slides
kaashoek@mit.edu

## Slide 2: Outline
Segment, Paging
LA, VA, PA
VM in xv6
  Initial page table
  Kernel page table
  User page table
Page Fault

## Slide 3: Review: ExoKernel
User-Mode
Kernel-Mode
DOS
UNIX
MicroKernel
ExoKernel
OS
App
Logic
Notes: Q1: what are difference? Consider file system, page fault handler, device driver, cpu scheduling
Q2: what is address space? Note that the kernel and apps share the same space
Q3: which one has the best performance
Q4: what is virtual machine’s architecture? Both Xen and KVM

## Slide 4: Virtual Memory

## Slide 5: Recap: Integrating Caches and VM
CPU
Trans-
lation
Cache
Main
Memory
VA
PA
miss
hit
data

## Slide 6
VA
CPU
MMU
PTEA
PTE
PA
Data
Memory
PA
PA
miss
PTEA
PTEA
miss
PTEA
hit
PA
hit
Data
PTE
L1
cache
CPU Chip
Recap: Integrating Caches and VM

## Slide 7: Translating with a k-level Page Table
VPN 1
0
p-1
n-1
VPO
VPN 2
...
VPN k
PPN
0
p-1
m-1
PPO
PPN
VIRTUAL ADDRESS
PHYSICAL ADDRESS
...
...
Level 1
page table
Level 2
page table
Level k
page table

## Slide 8: Page Table Entry (PTE)
P: present
R/W: readable / writable
U/S: user / supervisor
WT: write-through (1) / write-back (0)
CD: cache disabled
A: accessed (set by CPU, clear by OS)
D: dirty
PAT: page table attribute index
G: global page (no TLB updating on the address if CR3 is reset)
Notes: The Global, or 'G' above, flag, if set, prevents the TLB from updating the address in its cache if CR3 is reset. Note, that the page global enable bit in CR4 must be set to enable this feature.
A: Note that, this bit will not be cleared by the CPU, so that burden falls on the OS (if it needs this bit at all).

## Slide 9: Page Table Entry (PDE)
PS: page size (0=4KB, 1=4MB)
  4MB: super page

## Slide 10: Question
When the CPU is setting dirty bit of PTE, will it also set the dirty bit of corresponding PDE?
  Let’s check the manual!

## Slide 11: Quiz#1
In IA32 architecture, when the CR4_PSE bit in %cr4 register is set, then superpage mode is enabled, and the operating system can use either 4KB sized page or 4MB sized page. There are tradeoffs between small page and large page.
Consider the following scenarios:
a) Dump the content of a large file of several hundred megabytes mapped to the RAM by mmap() function to another location:
memcpy(addr_of_new_location, addr_of_mapped_file, sizeof_file);
b) Do the following calculation, where A, B are int pointers:
for(i=0; i<0x40000; ++i){
A[i] += B[i] & 0x3FFFFF;
}
Which sized (4KB or 4MB) page performs better in each scenario? Give your reasons.
Notes: For a), 4MB sized page performs better. Since the workload is data-intensive, using 4MB sized page will make the TLB more efficient, which avoids the costly TLB misses and reduces the average address translation time.
For b), 4KB sized page performs better. Since the workload is small and CPU-intensive, using 4KB sized page will have more effective memory use.

## Slide 12: PAE: Physical Address Extension
Enabled when
  CR0.PG=1 && CR4.PAE=1
32-bit linear address -> 36-bit physical address
  Can be more than 36
Maintains a set of 4 PDPTE registers
  Page directory pointer table
64-bit PTE
  Instead of 32-bit

## Slide 13: Address translation: PAE-4k

## Slide 14: Address translation: PAE-2M
Question: Why 2M instead of 4M?

## Slide 18: big picture of xv6's virtual addressing scheme
0x00000000:0x80000000
  user addresses below KERNBASE
0x80000000:0x80100000
  map low 1MB devices (for kernel)
0x80100000:?
  kernel instructions/data
? :0x8E000000
  224 MB of DRAM mapped here
0xFE000000:0x00000000
  more memory-mapped devices

## Slide 19: 4 KB pages
entrypgdir was simple
  array of 1024 PDEs, each mapping 4 MB but 4 MB is too large a page size!
  very wasteful if you have small processes xv6 programs are a few dozen kilobytes
  4 MB pages require allocating full 4 MB of phys mem
  solution: x86 MMU supports 4 KB pages
kvmalloc

## Slide 21: Setup_kvm
Usage
  creates a page table
  install mappings the kernel will need
  will be called once for each new process
Process
  must allocate PD, allocate some PTs, put mappings in PTEs
  alloc allocates a physical page for the PD
    returns that page's virtual address above 0x8000000
    so we'll have to call V2P before installing in cr3
  memset so that default is no translation (no P bit)
  a call to mappages for each entry in kmap[]

## Slide 23: what is kmap[]?
an entry for each region of kernel virtual address space
same as address space setup from earlier in lecture
  0x80000000 -> 0x00000000 (memory-mapped devices)
  0x80100000 -> 0x00100000 (kernel instructions and data)
  data -> data-0x80000000 (phys mem after where kernel was loaded)
  DEVSPACE -> DEVSPACE (more memory mapped devices)
  note no mappings below va 0x80000000 -- future user memory there

## Slide 26: mappages
arguments are PD, va, size, pa, perm
adds mappings from a range of va's to corresponding pa's
rounds because other uses pass in non-page-aligned addresses
for each page-aligned address in the range
call walkpgdir to find address of PTE need the PTE's address (not just content) because we want to modify

## Slide 28: walkpgdir
mimics how the paging h/w finds the PTE for an address
a little complex since xv6 allocates page-table pages lazily
  might not be present, might have to allocate
PDX extracts top ten bits
&pgdir[PDX(va)] is the address of the relevant PDE
now *pde is the PDE
if PTE_P
  the relevant page-table page already exists
  PTE_ADDR extracts the PPN from the PDE
  p2v() adds 0x80000000, since PTE holds physical address
if not PTE_P
  alloc a page-table page
  fill in PDE with PPN -- thus v2p
now the PTE we want is in the page-table page
  at offset PTX(va) , which is 2nd 10 bits of va

## Slide 31: User VM mapping
Create a process
  Inituvm : initialized user VM
  Loaduvm: load program segment
Context switch
  switchuvm
Grow/shrink/free VM
  allocuvm
  deallocuvm
  Freeuvm
Fork
  copyuvm