## Slide 1: Virtualization: I/O
Yubin Xia
Software School
Shanghai Jiao Tong University
Some Slides adapted from VMWare’s academic course plan

## Slide 2: Review: CPU Virtualization
Trap and Emulation
Instruction Interpretation
Binary Translation
Para-virtualization
New Hardware (to fix the 17 instructions)

## Slide 3: I/O Virtualization

## Slide 4: Device Virtualization
Emulated
Para-virtualized
Direct Access (Passthrough)
Hardware assisted I/O virtualization

## Slide 5: Emulated Device

## Slide 6: Abstraction & Virtualization
Real Disk
File
File
Virtualized Disk
Abstraction
Virtualization
Applications or OS
Application uses virtual disk as Real disk

## Slide 7: Emulated Devices
Emulate a device in class
  Emulated registers
  Memory mapped I/O or programmed I/O
Convert
  Intermediate representation
Back-ends per real device

## Slide 8: Serial Port Example
Monitor
Host OS
Serial Chip XYZ
LAN
User App
Guest
Serial Chip
ABC Driver
Serial Chip
ABC
Emulation
Generic Serial Layer

## Slide 9: Xen’s Domain-0 (Full-Virtualization)
Qemu for device emulation
  User-level application running in domain-0
  Implement NIC (e.g., 8139) in software
  Each VM has its own Qemu instance running
I/O request redirection
  Guest VM’s I/O requests are sent to domain-0
  Then Domain-0 sends to Qemu
  Eventually, Qemu will use domain-0’s NIC driver

## Slide 10: Emulated Devices
Positives
  Platform stability
  Allows interposition
  No special hardware support needed
    Isolation, multiplexing implemented by monitor
Negatives
  Can be slow
  Drivers needed in monitor or host

## Slide 11: Para-Virtualization

## Slide 12: Para-Virtualized Devices
Guest passes requests to Monitor at a higher abstraction level
  Monitor calls made to initiate requests
  Buffers shared between guest / monitor
Positives
  Simplify monitor
  Fast
Negatives
  Monitor needs to supply guest-specific drivers
  Bootstrapping issues

## Slide 13: Para-virtualized Devices: Front-end/Back-end
Para –virtualization
  Linux Guest
Hardware-supported virtualization
  Unmodified Windows
Isolated Device Drivers
Source: Ottawa Linux Symposium 2006 presentation.
http://www.cl.cam.ac.uk/netos/papers/

## Slide 14: VirtIO: Unified Para-virtualized I/O
Motivation: Linux has support for at least 8 virtualization platforms, each with its own para-virtualized I/O design/interfaces
VirtIO: to provide a unified I/O mode for para-virtualized device
  Adopted by KVM and lguest
Figure from: http://www.ibm.com/developerworks/cn/linux/l-virtio/figure2.gif

## Slide 15: Virtio in KVM
Virtio is a framework and set of drivers
  A hypervisor-independent, domain-independent, bus-independent protocol for transferring buffers
  A binding layer for attaching virtio to a bus (e.g., PCI)
  Domain specific guest drivers (networking, storage, etc.)
  Hypervisor specific host support

## Slide 22: Hardware assisted

## Slide 23: Directed I/O
Software-based sharing adds overhead to each I/O due to emulation layer
  This indirection has the additional affect of eliminating the use of hardware acceleration that may be available in the physical device.
Directed I/O has added enhancements to facilitate memory translation and ensure protection of memory that enables a device to directly DMA to/form host memory.
  Bypass the VMM’s I/O emulation layer
  Throughput improvement for the VMs

## Slide 24: Direct Access Device Virtualization
Allow Guest OS direct access to underlying device
Positives
  Fast
  Simplify monitor
    Limited device drivers needed
Negatives
  Need hardware support for safety (IOMMU)
  Need hardware support for multiplexing
  Hardware interface visible to guest
    Limits mobility of VM
  Interposition hard by definition

## Slide 25: Issues to Address
I/O address translation
  How to translate I/O address to host physical address
Interrupt mapping
  How to route an interrupt correctly to a guest VM
Device multiplexing
  How to multiplex a single hardware device among multiple VMs
Mostly importantly
  Provide strong isolation, while reduce hypervisor involvement

## Slide 26: VT-d: Intel® Virtualization Technology for Directed I/O
Provides the capability to ensure improved isolation of I/O resources for greater reliability, security, and availability.
Supports the remapping of I/O DMA transfers and device-generated interrupts.
Provides flexibility to support multiple usage models that may run un-modified, special-purpose, or "virtualization aware" guest OSs.

## Slide 27: Address Translation Services
VT-d architecture defines a multi-level page-table structure for DMA address translation
The multi-level page tables are similar to IA-32 processor page-tables, enabling software to manage memory at 4 KB or larger page granularity
Notes: VT-d architecture defines a multi-level page-table structure for DMA address translation.The multi-level page tables are similar to IA-32 processor page-tables, enabling software to manage memory at 4 KB or larger page granularity. Hardware implements the page-walk logic and traverses these structures using the address from the DMA request. The number of page-table levels that must be traversed is specified through the context-entry referencing the root of the page table. The page directory and page-table entries specify independent read and write permissions, and hardware computes the cumulative read and write permissions encountered in a page walk as the effective permissions for a DMA request. The page-table and page-directory structures are always 4 KB in size, and larger page sizes (2 MB, 1 GB, etc.) are enabled through super-page support.

## Slide 28: DMA Remapping
DMA-remapping translates the address of the incoming DMA request to the correct physical memory address and perform checks for permissions to access that physical address
DMA-remapping hardware logic in the chipset sits between the DMA capable peripheral I/O devices and the computer’s physical memory
Notes: Intel VT-d enables protection by restricting direct memory access (DMA) of the devices to pre-assigned domains or physical memory regions. This is achieved by a hardware capability known as DMA-remapping. The VT-d DMA-remapping hardware logic in the chipset sits between the DMA capable peripheral I/O devices and the computer’s physical memory. It is programmed by the computer system software. In a virtualization environment the system software is the VMM. In a native environment where there is no virtualization software, the system software is the native OS. DMA-remapping translates the address of the incoming DMA request to the correct physical memory address and perform checks for permissions to access that physical address, based on the information provided by the system software.
Intel VT-d enables system software to create multiple DMA protection domains. Each protection domain is an isolated environment containing a subset of the host physical memory. Depending on the software usage model, a DMA protection domain may represent memory allocated to a virtual machine (VM), or the DMA memory allocated by a guest-OS driver running in a VM or as part of the VMM itself. The VT-d architecture enables system software to assign one or more I/O devices to a protection domain. DMA isolation is achieved by restricting access to a protection domain's physical memory from I/O devices not assigned to it by using address-translation tables. This provides the necessary isolation to assure separation between each virtual machine’s computer resources.
When any given I/O device tries to gain access to a certain memory location, DMA remapping hardware looks up the address-translation tables for access permission of that device to that specific protection domain. If the device tries to access outside of the range it is permitted to access, the DMA remapping hardware blocks the access and reports a fault to the system software.

## Slide 29: VT-d Feature: Interrupt Remapping
The interrupt requests generated by I/O devices must be controlled by the VMM
When the interrupt occurs, the VMM must present the interrupt to the guest. This is not accomplished through hardware.
The VT-d interrupt-remapping architecture addresses this problem by redefining the interrupt-message format.
Interrupt requests specify a requester-ID and interrupt-ID, and remap hardware transforming these requests to a physical interrupt.
Notes: For proper device isolation in a virtualized system, the interrupt requests generated by I/O devices must be controlled by the VMM. In the existing interrupt architecture for Intel platforms, a device may generate either a legacy interrupt (which is routed through I/O interrupt controllers) or may directly issue message signaled interrupts (MSIs) [20]. MSIs are issued as DMA write transactions to a pre-defined architectural address range, and the interrupt attributes (such as vector, destination processor, delivery mode, etc.) are encoded in the address and data of the write request. Since the interrupt attributes are encoded in the request issued by devices, the existing interrupt architecture does not offer interrupt isolation across protection domains.
The VT-d interrupt-remapping architecture addresses this problem by redefining the interrupt-message format. The new interrupt message continues to be a DMA write request, but the write request itself contains only a "message identifier" and not the actual interrupt attributes. The write request, like any DMA request, specifies the requester-id of the hardware function generating the interrupt.
DMA write requests identified as interrupt requests by the hardware are subject to interrupt remapping. The requestor-id of interrupt requests is remapped through the table structure. Each entry in the interrupt-remapping table corresponds to a unique interrupt message identifier from a device and includes all the necessary interrupt attributes (such as destination processor, vector, delivery mode, etc.). The architecture supports remapping interrupt messages from all sources including I/O interrupt controllers (IOAPICs), and all flavors of MSI and MSI-X interrupts defined in the PCI specifications. (there is no mention of legacy interrupts) For more info about MSI refer to: http://lwn.net/Articles/44139/

## Slide 30: Interrupt Remapping

## Slide 31: Drawbacks to Directed I/O
One concern with direct assignment is that it has limited scalability
  A physical device can only be assigned to one VM.
  For example, a dual port NIC allows for direct assignment to two VMs. (one port per VM)
  Consider for a moment a fairly substantial server of the very near future
    4 physical CPU’s
    12 cores per CPU
    If we use the rule that one VM per core, it would need 48 physical ports.

## Slide 32: Device multiplexiing: Single Root I/O Virtualization
Single Root I/O Virtualization (SR-IOV) is a Peripheral Component Interconnect Special Interest Group (PCI-SIG) specification.
SR-IOV provides a standard mechanism for devices to advertise their ability to be simultaneously shared among multiple virtual machines.
SR-IOV allows for the partitioning of a PCI function into many virtual interfaces for the purpose of sharing the resources of a PCI Express* (PCIe) device in a virtual environment.
Notes: SRIOV it is not a feature, is a specification.

## Slide 33: Device multiplexiing: Single Root I/O Virtualization
With SR-IOV:
  SI’s will get direct access to PCIe device functions
  No more need for hypervisor (VI) to manage all system resources
PCIe devices will have multiple virtual functions (VF’s)
  utilizable by multiple SI’s
  a single SI may also use multiple virtual functions
Security of I/O Streams ensured by
  Independency of control structures between VF’s within one PCIe device
  I/O address translation services
  Interrupt remapping mechanisms
Notes: SRIOV it is not a feature, is a specification.

## Slide 34: Physical V.S. Virtual
Function 0
ATC1
Physical Resources1
Function 1
ATC2
Physical Resources2
Function 2
ATC3
Physical Resources3
Internal Routing
Configuration Resources
PCIe
Port
PCIe
Port
PCIe
Port
PCIe Device
PF 0
ATC1
Physical Resources
VF 0,1
Physical Resources
VF 0,2
Physical Resources
Internal Routing
PCIe
Port
PCIe SR-IOV
Capable Device
Configuration Resources
Physical
Virtual

## Slide 35: Single Root I/O Virtualization

## Slide 36: Intel Virtualization Technology Evolution
Hardware support for IO-device virtualization
Device DMA remapping
Direct assignment of I/O devices to VMs
Interrupt Routing and Remapping
VT-d
VMM Software
Evolution
Past No Hardware Support
VMM software evolution over time with hardware support
Software-only VMMs
Binary translation
Paravirtualization
Simpler and more Secure VMM through foundation of virtualizable ISAs
Vector 3: I/O Focus
PCI-SIG
Standards for IO-device sharing:
Multi-Context I/O Devices
Endpoint Address Translation Caching
Under definition in the PCI-SIG* IOVWG
Vector 1: Processor Focus
Vector 2: Platform Focus
Establish foundation for virtualization in the IA-32 and Itanium architectures…
VT-x
VT-i
… followed by on-going evolution of support:
Micro-architectural (e.g., lower VM switch times)
Architectural (e.g., Extended Page Tables)
Increasingly better CPU and I/O virtualization performance and functionality as I/O devices and VMMs exploit infrastructure provided by VT-x, VT-i, VT-d
*Other names and brands may be claimed as the property of others
Today

## Slide 37: Summary

## Slide 38: Computer System Organization
CPU
MMU
Memory
Controller
Local Bus
Interface
High-Speed
I/O Bus
NIC
Controller
Bridge
Frame Buffer
LAN
Low-Speed
I/O Bus
USB
CD-ROM

## Slide 39
Application
TCP/IP Stack
Device Driver (8139)
TCP/IP Stack
Real Device Driver
Physical Device
Guest Domain
Domain-0
Xen
Hardware
Qemu (User-level)

## Slide 40
Application
TCP/IP Stack
Frontend Dev Driver
TCP/IP Stack
Backend Dev Driver
Real Device Driver
Split Device Driver
Physical Device
Guest Domain
Domain-0
Xen
Hardware

## Slide 41: Summary of I/O Virtualization
CPU
MMU
Memory
Controller
Local Bus
Interface
High-Speed
I/O Bus
NIC
Controller
Bridge
Frame Buffer
LAN
Low-Speed
I/O Bus
USB
CD-ROM
VM
Guest OS

## Slide 42: Memory Isolation w/ Direct Access Device
CPU
MMU
Memory
Controller
Local Bus
Interface IOMMU
High-Speed
I/O Bus
NIC
Controller
Bridge
Frame Buffer
LAN
Low-Speed
I/O Bus
USB
CD-ROM
VM
Guest OS

## Slide 43: Virtualization Enabled Device
CPU
MMU
Memory
Controller
Local Bus
Interface IOMMU
High-Speed
I/O Bus
NIC
Controller
Bridge
Frame Buffer
LAN
Low-Speed
I/O Bus
USB
CD-ROM
VM1
Guest OS
vNIC 1
VM2
Guest OS
vNIC 2

## Slide 44: Control Flow of Pressing ‘a’ and Displaying ‘a’
Keyboard triggers an interrupt. (Suppose currently VM is running)
VMExit! Jump to host Linux’s interrupt handler (non-root -> root)
Host Linux driver gets the character ‘a’
Host Linux returns to Qemu (kernel -> user)
Qemu notices an I/O inputs in its main loop, updates its emulated keyboard device states (write ‘a’ to an emulated register of the emulated keyboard)
Qemu puts a virtual interrupt in guest’s VMCS, and use ioctl to resume VM (user -> kernel) (root -> non-root)

## Slide 45: Control Flow of Pressing ‘a’ and Displaying ‘a’
VM finds the keyboard interrupt, jumps to interrupt handler (user -> kernel)
VM driver starts to run, it tries to read keyboard’s register to find out which key is pressed, by ‘in 0x100 %eax’, which will trap (non-root -> root)
VMExit! Host Linux gives control to Qemu (kernel -> user)
Qemu finds the reason is I/O instruction, then retrieves the instruction and emulates it, by reading the states of emulated keyboard, gets a value ‘a’ (which is just written by Qemu itself)
Qemu updates VMCS->eax, and starts to run VM (user-> kernel) (root -> non-root)
VM resumes and gets the value in %eax, which is ‘a’
Guest OS returns the value to user application (kernel -> user)

## Slide 46: Virtualization Techs
Virtualization | Software Solution | Hardware Solution
CPU | Trap & Emulate Instruction interpretation Binary translation Para-virtualization: no 17 insns | VT-x Root / non-root mode VMCS
Memory | Shadow page table Separating page tables for U/K Para-virtualization: Direct paging | EPT
I/O | Direct I/O Device emulation Para-virtualization: Front-end & back-end driver (e.g., virtio) | IOMMU SR-IOV

## Slide 47: for Security

## Slide 48: Virtualization Preliminary: VT-x
VM
Hypervisor
host mode
guest mode
VM entry
VM exit
Ring 0
Ring 3
Notes: Besides traditional privilege rings on the processor, VT-x introduced a new host mode.
Hypervisor is designed to run in host mode. All privileged operations in guest mode would cause trap into host mode, ie, Vmexit.

## Slide 49: Interposition with CloudVisor
VM
Cloudvisor
host mode
guest mode
VM entry
VM exit
Hypervisor
VM entry
VM exit
Ring 0
Ring 3
Notes: Cloudvisor interposes hypervisor and vms...
In this way, some sensitive states (general purposed registers) could be saved during VMExit.

## Slide 50: SGX : Isolated Execution
Application keeps its data/code inside the “enclave”
  Smallest attack surface by reducing TCB (App + processor)
  Protect app’s secret from untrusted privilege software (e.g., OS, VMM)
CPU Package
System Memory
Enclave
Memory
Encryption
Engine (MEE)
Snooping
Access from
OS/VMM
Encrypted
code/data
Notes: SGX allows part of application code to run in isolation inside an enclave. The enclave region of the main memory is encrypted. The content is only decrypted inside the CPU package using processor specific keys. Thus, even if a malicious adversary has full control over the hardware, it cannot access/modify the enclave. Also, the enclave is protected from other software running in the host, including the OS and hypervisor. In summary, the TCB is the CPU package and the application code running inside and enclave.